## Slide 1: SEP 728 Project
IIoT Solution for a Steel and Wood Manufacturing Factory
By:
Daniel Hilal
Kunal Garg

## Slide 2: Outline
Project Requirements
  Factory Machines
Solution Architecture
  Why MQTT with Sparkplug B
  Why Ignition
  Why AWS
  Integration: MQTT, Sparkplug B, Ignition and AWS
Implementation
  Simulating PLC and HMI
  Simulating IoT Sensors
  Simulating OPC UA Server
  Publishing Data to Broker
  Developing SCADA Project
  Mobile Application SCADA
  Alarm Notifications
References

## Slide 3: Project Requirements
Overview: Architecting an IIoT solution, tailored for steel and wood manufacturing machines, to improve and have a better understanding of their performance and safety.
Collecting data from the control system of steel and wood manufacturing machines
Collecting data from external sensors
Using the data collected to display useful information and issue alerts and control commands to the plant floor

## Slide 4: Factory Machines
CNC Router - BIESSE ROVER A 1332 ATS
Edge Bending Machine - HOLZHER LUMINA 1586
Sanding Machine - HEESSEMAN BM8
Automated Painting Booth - CEFLA MITO
VEIL PAINTING BOOTH

## Slide 5: Solution Architecture

## Slide 6: Why MQTT with Sparkplug B
MQTT (Message Queue Telemetry Transport) is a lightweight message protocol that is based on a subscription-publishing model.
Sparkplug B formats the MQTT message to be easily managed and discovered.
Designed for industrial applications:
  Extremely lightweight
  Energy efficient
  Secure
  Data-agnostic
  Easily implemented
Notes:   Clients do not have addresses like in email systems, and messages are not sent to clients.
  Messages are published to a broker on a topic.
  The job of an MQTT broker is to filter messages based on topic, and then distribute them to subscribers.

## Slide 7: Why Ignition
Server Based
Cross Platform
Simple Licensing
Notes: Server Based: One computer controls everything
Simple Licensing: One license for the server gives you unlimited access, such as unlimited Clients, unlimited Tags, and unlimited projects.
Cross Platform: Ignition works with any major operating system, even iOS and Android.

## Slide 8: Why Ignition
Web-based Deployment
Web-launched Designer and Client
Notes: Web-based Deployment: Ignition is installed, deployed, and managed using standard web technologies.
Web-launched Designer and Client: Ignition's Designer tool and runtime clients and sessions are launched using the web.

## Slide 9: Why Ignition
Scalable Modular Architecture
Built-in Security
Notes: Scalable Modular Architecture: Create a scalable and centrally managed SCADA system using Ignition's web-based server architecture.
Built-in Security: Security is built in to every aspect of Ignition.

## Slide 10: Why AWS
Notes: Authentication: X.509 client certificate
Port: 8883

## Slide 11: Why AWS
AWS broker:
  AWS IoT manages device communication through a message broker.
  This broker can also forward messages to the AWS IoT rules engine, which can act on the content of the message.
AWS security:
  Device connections to AWS IoT use X.509 client certificates and AWS signature V4 for authentication.
  Device communications are secured by TLS version 1.2
  AWS IoT requires devices to send the Server Name Indication (SNI) extension when they connect.
AWS device endpoints that support specific device-centric IoT functions, services and security.
Notes: Authentication: X.509 client certificate
Port: 8883

## Slide 12: Why AWS
AWS Rules:

## Slide 13: Integration: MQTT, Sparkplug B, Ignition and AWS

## Slide 14: Implementation

## Slide 15: Simulating PLC and HMI

## Slide 16: Simulating IoT Sensors

## Slide 17: Simulating OPC UA Server

## Slide 18: Publishing Data to Broker

## Slide 19: Creating SCADA Project

## Slide 20: Developing SCADA Project

## Slide 21: Mobile Application SCADA

## Slide 22: Alarm Notifications

## Slide 23: References
AWS, “AWS IOT SiteWise Documentation,” Amazon Documentation. [Online]. Available: https://docs.aws.amazon.com/iot-sitewise/. [Accessed: 01-Dec-2021].
AWS, “AWS IOT Core Documentation,” Amazon Documentation, 2017. [Online]. Available: https://docs.aws.amazon.com/iot/index.html. [Accessed: 01-Dec-2021].
Cirrus Link, “SCADA system - AWS Cloud,” Cirrus Link Solutions, 12-Oct-2021. [Online]. Available: https://cirrus-link.com/aws-cloud/. [Accessed: 01-Dec-2021].
Cirrus Link, “SCADA system - MQTT software for IIOT,” Cirrus Link Solutions, 08-Apr-2021. [Online]. Available: https://cirrus-link.com/mqtt-software-for-iiot-scada/. [Accessed: 01-Dec-2021].
Eclipse Foundation, “Sparkplug™ Specification.” [Online]. Available: https://www.eclipse.org/tahu/spec/Sparkplug%20Topic%20Namespace%20and%20State%20ManagementV2.2-with%20appendix%20B%20format%20-%20Eclipse.pdf. [Accessed: 01-Dec-2021].
Inductive Automation, “Ignition Platform - Ignition User Manual 8.1,” Ignition Documentation. [Online]. Available: https://docs.inductiveautomation.com/display/DOC81/Ignition+Platform. [Accessed: 01-Dec-2021].
Inductive Automation, “Ignition Modules - Ignition User Manual 8.1,” Ignition Documentation. [Online]. Available: https://docs.inductiveautomation.com/display/DOC81/Ignition+Modules. [Accessed: 01-Dec-2021].
Node-RED, “User Guide,” Node-RED Documentation. [Online]. Available: https://nodered.org/docs/user-guide/. [Accessed: 01-Dec-2021].
OASIS Open, “MQTT 3.1.1 Specification,” MQTT Version 3.1 - Oasis, 29-Oct-2014. [Online]. Available: https://docs.oasis-open.org/mqtt/mqtt/v3.1.1/os/mqtt-v3.1.1-os.pdf. [Accessed: 01-Dec-2021].

## Slide 24: Thank you!